## Slide 1: Computer Architecture ----A Quantitative Approach
陈文智
浙江大学计算机学院
chenwz@zju.edu.cn

## Slide 2: Topics in Chapter 1
1.1 Introduction
1.2 Classes of computers
1.3 Defining computer architecture and What’s the task of computer design?
1.4 Trends in Technology
1.5 Trends in power in Integrated circuits
1.6 Trends in Cost
1.7 Dependability
1.8 Measuring, Reporting and summarizing Perf.
1.9 Quantitative Principles of computer Design
1.10 Putting it altogether

## Slide 3: History of the Computer
Original:
  Big Fishes Eating Little Fishes

## Slide 4: Computer Food Chain
PC
Work-
station
Mini-
computer
Mainframe
Mini-
supercomputer
Supercomputer
Massively Parallel Processors

## Slide 5: Computer Food Chain
Mini-
supercomputer
Massively Parallel Processors
Mini-
computer
PC
Work-
station
Mainframe
Supercomputer
Server
Embedded system

## Slide 7: Incredible performance improvement
Chart: Performance(vs. VAX-11/780)
| 1978 | 1980 | 1982 | 1984 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006
东部 | 1.5 | 5 | 9 | 13 | 18 | 24 | 51 | 80 | 117 | 183 | 280 | 481 | 649 | 993 | 1267 | 1779 | 2584 | 4195 | 5364 | 5764 | 6505
25% /year
52%/year
20%/year

## Slide 8: Conclusion
Technological improvements more steady than progress in computer architecture
After RISC emergence, computer design emphasized both architectural innovation and efficient use of technology improvements.
  CA plays an important role in performance Improvement
Little ILP left to exploit due to power dissipation
  Faster uniprocessor => multiple processor on chip
  ILP => TLP and DLP
  Implicitly, compiler and hardware => Explicitly, programmer

## Slide 9: MIPS
Process ability  New Applications
1975
1980
1985
1990
1995
2000
10,000
1,000
10
100
1
0.1
MIPS
8086
Pentium ® IV
80286
i386
i486
Pentium®
Pentium ® II
Pentium ® III

## Slide 10: Why Such Change in 60 years?
Two reasons:
  Advances in the technology used to build computers
    IC
    Storage device(including RAM and DISK)
    Peripheral device
  Innovation in computer design
    Simple  complex  most complex  simple  complex  most complex
    Sometimes rapid, sometimes slow
    Many technology have been washed out

## Slide 11: Four Decades of microprocessor
The Decade of the 1970’s “Microprocessors”
  - Programmable Controller
  - Single-Chip Microprocessors
  - Personal Computers (PC)
The Decade of the 1980’s “Quantitative Architecture”
  - Instruction Pipelining
  - Fast Cache Memories
  - Compiler Considerations
  - Workstations
The Decade of the 1990’s “Instruction-Level Parallelism”
  - Superscalar Processors
  - Speculative Microarchitectures
  - Aggressive Code Scheduling
  - Low-Cost Desktop Supercomputing
The Decade of the 2000’s “Thread-level/Data-level parallelism”

## Slide 12: Forces on Computer Architecture
Computer Architecture:
• Instruction Set Design
• Organization
• Hardware/Software Boundary
Technology
Programming
Languages
Operating
Systems
History
Applications
Interface Design
(ISA)
Measurement & Evaluation
Parallelism
Compilers
Computer architecture has been at the core of such technological development and is still on a forward move

## Slide 13: Topics in Chapter
1.1 Introduction
1.2 Classes of computers
1.3 Defining computer architecture and What’s the task of computer design?
1.4 Trends in Technology
1.5 Trends in power in Integrated circuits
1.6 Trends in Cost
1.7 Dependability
1.8 Measuring, Reporting and summarizing Perf.
1.9 Quantitative Principles of computer Design
1.10 Putting it altogether

## Slide 14: Classes of computers
Flynn’s Taxonomy: A classification of computer architectures based on the number of streams of instructions and data

## Slide 15: SISD
A serial (non-parallel) computer
Single instruction: only one instruction stream is being acted on by the CPU during any one clock cycle
Single data: only one data stream is being used as input during any one clock cycle
Deterministic execution
This is the oldest and until recently, the most prevalent form of computer
Examples: most PCs, single CPU workstations and mainframes
CU
MU
PU
I/O
IS
DS
IS

## Slide 16: SIMD
A type of parallel computer
Single instruction: All processing units execute the same instruction at any given clock cycle
Multiple data: Each processing unit can operate on a different data element
This type of machine typically has an instruction dispatcher, a very high-bandwidth internal network, and a very large array of very small-capacity instruction units.
Best suited for specialized problems characterized by a high degree of regularity, such as image processing.
Synchronous (lockstep) and deterministic execution
Two varieties:
  Processor Arrays: Connection Machine CM-2, Maspar MP-1, MP-2
  Vector Pipelines: IBM 9000, Cray C90, Fujitsu VP, NEC SX-2, Hitachi S820

## Slide 17: SIMD
CU
PU1
IS
IS
PUn
DS
DS
MM1
MMn

## Slide 18: MISD
A single data stream is fed into multiple processing units.
Each processing unit operates on the data independently via independent instruction streams.
Few actual examples of this class of parallel computer have ever existed. One is the experimental Carnegie-Mellon C.mmp computer (1971).
Some conceivable uses might be:
  multiple frequency filters operating on a single signal stream
  multiple cryptography algorithms attempting to crack a single coded message.

## Slide 19: MISD
DS
CU1
PE1
IS
PEn
CUn
……
IS
…
MM1
MMn
…
……
DS
I/O

## Slide 20: MIMD
Currently, the most common type of parallel computer. Most modern computers fall into this category.
Multiple Instruction: every processor may be executing a different instruction stream
Multiple Data: every processor may be working with a different data stream
Execution can be synchronous or asynchronous, deterministic or non-deterministic
Examples: most current supercomputers, networked parallel computer "grids" and multi-processor SMP computers - including some types of PCs.

## Slide 21: MIMD
I/O
CU1
PE1
IS
PEn
CUn
IS
…
SM
…
MM1
MMn
…
IS
IS
I/O

## Slide 22: Classification-market
PC
Work-
Station
1980s-2000s
Mini-
Computer
1970s
Mainframe
1960s
Mini-
Supercomputer
1970s
Supercomputer
1970s
Massively Parallel Processors
1980s
Embedded system
2000s
Server
2000s

## Slide 23: Effect of dramatic performance growth
Enhanced the capability available to computer users.
Microprocessor-based computers across the entire range of the computer design.
  Minicomputer => servers using microprocessors
  Mainframe => multiprocessors consisting of microprocessors
  Supercomputer => multiprocessor collections

## Slide 24: Four computing markets
Feature | Mobile | Desktop | Server | Embedded
Price of system | $100–$1000 | $300–$2500 | $5000 -$5,000,000 | $10 -$100,000
Price of microprocessor module | $10–$100 | $50-$500 per proc. | $200 -$10,000 per proc. | $0.01 -$100 per proc.
Critical system design issues | Cost, energy, media performance, responsiveness | Price-perf. Graphics perf. | Throughput, availability, scalability, energy | Price, Power consumption, application-specific perf.

## Slide 25: Desktop Computing
The first, and still the largest market in dollar terms, is desktop computing.
Requirement:
  Optimized price-performance
New challenges:
  Web-centric, interactive application
  How to evaluate performance?

## Slide 26: Servers
The role of servers to provide larger scale and more reliable file and computing services grew.
  For servers, different characteristics are important. First, dependability is critical.
  A second key feature of server systems is an emphasis on scalability.
  Lastly, servers are designed for efficient throughput.

## Slide 27: Internet of Things/Embedded Computers
Have the widest spread of processing power and cost.
  8-bit 16-bit 32-bit 64-bit
Real time performance (soft & hard)
Strict resource constraints
  limited memory size, lower power consumption,...
The use of processor cores together with application-specific circuitry.
  DSP, mobile computing

## Slide 28: Personal Mobile Device
Share many of the characteristics of desktop computers.
  Web-based and media-oriented
  Ability to run third-party software (APPs)
    major difference with embedded computers
Energy efficiency
  Battery powered, absence of a fan
Low-cost
Real-time performance requirement
Notes: Personal mobile device (PMD) is the term we apply to a collection of wireless
devices with multimedia user interfaces such as cell phones, tablet computers,
and so on. Cost is a prime concern given the consumer price for the whole
product is a few hundred dollars. Although the emphasis on energy efficiency
is frequently driven by the use of batteries, the need to use less expensive packag-
ing—plastic versus ceramic—and the absence of a fan for cooling also limit total
power consumption. We examine the issue of energy and power in more detail
in Section 1.5. Applications on PMDs are often web-based and media-oriented,
like the previously mentioned Google Translate example. Energy and size
requirements lead to use of Flash memory for storage (Chapter 2) instead of
magnetic disks.
The processors in a PMD are often considered embedded computers, but we
are keeping them as a separate category because PMDs are platforms that can
run externally developed software, and they share many of the characteristics of
desktop computers. Other embedded devices are more limited in hardware and
software sophistication. We use the ability to run third-party software as the divid-
ing line between nonembedded and embedded computers.
Responsiveness and predictability are key characteristics for media applica-
tions. A real-time performance requirement means a segment of the application
has an absolute maximum execution time. For example, in playing a video on a
PMD, the time to process each video frame is limited, since the processor must
accept and process the next frame shortly. In some applications, a more nuanced
requirement exists: the average time for a particular task is constrained as well as
the number of instances when some maximum time is exceeded. Such
approaches—sometimes called soft real-time—arise when it is possible to miss
the time constraint on an event occasionally, as long as not too many are missed.
Real-time performance tends to be highly application-dependent.
Other key characteristics in many PMD applications are the need to minimize
memory and the need to use energy efficiently. Energy efficiency is driven by both
battery power and heat dissipation. The memory can be a substantial portion of the
system cost, and it is important to optimize memory size in such cases. The impor-
tance of memory size translates to an emphasis on code size, since data size is dic-
tated by the application.

## Slide 29: Questions
What we need to design for different computing markets?
What a computer Architecture designer need to know ?

## Slide 30: Topics in Chapter
1.1 Why take this course ?
1.2 Classes of computers in current computer market
1.3 Defining computer architecture and What’s the task of computer design.
1.4 Trends in Technology
1.5 Trends in power in Integrated circuits
1.6 Trends in Cost
1.7 Dependability
1.8 Measuring, Reporting and summarizing Perf.
1.9 Quantitative Principles of computer Design
1.10 Putting it altogether

## Slide 31: What computer architecture is all about
What are the components of a computer?
How to effectively put together the various components

## Slide 32: Original Concept of Computer architecture
The attributes of a [computing] system as seen by the programmer, i.e.,
The conceptual structure and functional behavior, as distinct from the organization of the data flows and controls the logic design, and the physical implementation.
  Amdahl, Blaaw, and Brooks, 1964

## Slide 33: Instruction Set Architecture (ISA)

## Slide 34: ISA: the interface between hardware and software
Purpose 1: (now irrelevant)
  Re-use of fixed hardware resources
Purpose 2:
  Interface between developer and hardware
  Contract from one chip generation and the next
instruction set
software
hardware

## Slide 35: Evolution of Instruction Sets
Single Accumulator (EDSAC 1950)
Accumulator + Index Registers
(Manchester Mark I, IBM 700 series 1953)
Separation of Programming Model
from Implementation
High-level Language Based
Concept of a Family
(B5000 1963)
(IBM 360 1964)
General Purpose Register Machines
Complex Instruction Sets
Load/Store Architecture
(Vax, Intel 432 1977-80)
(CDC 6600, Cray 1 1963-76)
(Mips,Sparc,HP-PA,IBM RS6000, . . .1987)
RISC

## Slide 36: Interface Design
A good interface:
  Lasts through many implementations (portability, compatibility)
  Usable in many different scenarios (generality)
  Provides convenient functionality to higher levels
  Permits an efficient implementation at lower levels

## Slide 37: Seven dimensions of ISA
Class
Memory addressing
Addressing modes
Types and sizes of operands
Operations
Control flow instructions
Encoding

## Slide 38: Evolution of Computer Architecture Course
1950s to 1960s:
  Computer Arithmetic
1970s to mid 1980s:
  Instruction Set Design, especially ISA appropriate for compilers
1990s:
  Design of CPU, memory system, I/O system, Multiprocessors, Networks.
2010s:
  Multicore, Self adapting systems? Self organizing structures?
  Power-aware design, reconfigurable
2020s:
  Heterogeneous accelerator, GPU, FPGA
  Security design

## Slide 39: Computer Architecture
Computer Architecture is the science and art of selecting and interconnecting hardware components to create computers that meet functional, performance and cost goals.
It Covers:
  Instruction Set design
  Organization: high level of aspects of a computer’s design
    Memory, memory interconnect, internal CPU
  Hardware: specifics of computer
    Detailed logic design, packaging, cooling system, board displacement, power

## Slide 40: Computer Architecture Topics
Instruction Set Architecture
Pipelining, Hazard Resolution,
Superscalar, Reordering,
Prediction, Speculation,
Vector, Dynamic Compilation
Addressing,
Protection,
Exception Handling
L1 Cache
L2 Cache
DRAM
Disks, WORM, Tape
Coherence,
Bandwidth,
Latency
Emerging Technologies
Interleaving
Bus protocols
RAID
VLSI
Input/Output and Storage
Memory
Hierarchy
Pipelining and Instruction
Level Parallelism
Network
Communication
Other Processors

## Slide 41: Computer Architecture Topics
M
Interconnection Network
S
P
M
P
M
P
M
P
° ° °
Topologies,
Routing,
Bandwidth,
Latency,
Reliability
Network Interfaces
Shared Memory,
Message Passing,
Data Parallelism
Processor-Memory-Switch
Multiprocessors
Networks and Interconnections

## Slide 42: The Task of Computer Design 1
Define the user requirement:
  Functional requirement: Fig1.4
    Application area
    Level of software compatibility
    OS requirements
    Standards
  Nonfunctional requirements:
    Price/performance
    Availability, scalability, throughput, ...
    Power, size, memory, temperature, ...

## Slide 43: Application Performance
1996 - 1997
  CPU performance improves by N = 400/200 = 2
  program performance improves by N = 100/55 = 1.81
1997 - 1998
  CPU performance - factor of 2
  program performance N = 55/32.5 = 1.7
1998 - 1999
  CPU performance - factor of 2
  program performance N = 32.5 / 21.25 = 1.53
1999 - 2000
  CPU Performance - factor of 2
  program performance N = 21.25 / 15.6 = 1.36

## Slide 44: Performance for Web Surfing
Assume 50% CPU, 50% I/O
1996 - 1997
  CPU performance improves by N = 400/200 = 2
  Program performance improves by N = 100/75 = 1.33
1997 - 1998
  CPU performance *= 2
  Program performance N = 75/62.5= 1.2
1998 - 1999
  CPU performance *= 2
  Program performance N = 62.5/56.5 = 1.11

## Slide 45: Computer Applications
Architects need to understand applications’ behavior
  We say we design general purpose processors, but we should also focus on specific sets of applications
  Architecture can be tuned for applications
Types of applications today
  Scientific
    Weather prediction, crash analysis, earthquake analysis, medical imaging, imaging of the earth (searching for oil)
  Business
    database, data mining, video
  General purpose
    Microsoft Word, Excel
  Real-time
    automated control systems,
  Others: Games, Mobile

## Slide 46: Architectures are Tuned to Applications
HP’s: 1.5 MB cache for transaction processing
Alpha: very fast FP for scientific
StrongARM: embedded
Intel MMX: multimedia
Sony EE: graphics rendering
Applications drive the design of the processor

## Slide 47: The Task of Computer Design 2
Determine the important attributes of a new machine to maximize performance while staying with constrains, such as cost, power, availability, etc.
  instruction set architecture design
  functional organization
    High level aspects of computer design, i.e. memory system, bus architecture and internal CPU design.
  logic design (hardware)
  implementation (hardware)

## Slide 48: Trend of Architecture
Emerging issues
  High Speed
  Multi-issue (superscalar) / Multithreading / Multiprocessor
  CPU Cores / Multiple cores
  Embedded
  IRAM
Emerging applications
  Digital media / Digital library
  Toaster on the internet
  Wireless everything
  Star Trek communicator
  Intelligent appliances & agents

## Slide 49: Computer Engineering Methodology
Evaluate Existing
Systems for
Bottlenecks !
Technology
Trends
Benchmarks
User
requirement
Quantitative Principles
Simulate New
Designs and
Organizations
Workloads
Implement Next
Generation System

## Slide 50: Computer Design life cycle
Quantitative
principle
Evaluate Existing
Systems for
Bottlenecks
Simulate New
Designs and
Organizations
Implement Next
Generation System
Technology
Trends
Benchmarks
Workloads
Implementation
Complexity
Requirements

## Slide 51: Summary:Task of computer design
Considerations:
  Functional and non functional requirements
  Implementation complexity
    Complex designs take longer to complete
    Complex designs must provide higher performance to be competitive
  Technology trends
    Not only what's available today, but also what will be available when the system is ready to ship. (more on this later)
  Trends in Power in IC
  Trends in cost
Arguments
  Evaluate Existing Systems for Bottlenecks
Quantitative Principles

## Slide 52: Topics in Chapter
1.1 Why take this course ?
1.2 Classes of computers in current computer market
1.3 Defining computer architecture and What’s the task of computer design?
1.4 Trends in Technology
1.5 Trends in power in Integrated circuits
1.6 Trends in Cost
1.7 Dependability
1.8 Measuring, Reporting and summarizing Perf.
1.9 Quantitative Principles of computer Design
1.10 Putting it altogether

## Slide 53: Technology Trends
Moore Law
  In 1965 he predicted that the number of components the industry would be able to place on a computer chip would double every year. In 1975, he updated his prediction to once every two years. It has become the guiding principle for the semiconductor industry to deliver ever-more-powerful chips while decreasing the cost of electronics.
Gordon Moore

## Slide 54: Technology Trends
Integrated circuit logic technology
  Transistor Density: incr. 35% per year, (4x every 4 years)
  Die size: 10%-20% per year
  Transistor count per chip:40-55% per year
Semiconductor DRAM
  Capacity: 40% per year (2x every 2 years)
  Memory speed: about 10% per year
Magnetic Disk tech.
  Density: 30% per year before 1990;60% per year in1990-1996
  100% per year in 1996-2004;30% per-year after 2004
  capacity: about 60% per year
Network bandwidth
  10Mb  100Mb  1Gb
  10 years 5 years
Designers often design for the next technology.

## Slide 55: Notes
A rule of thumb
  Cost decrease rate ~ density increase rate
Technology thresholds
  Technology improves continuously, an impact of this improvements can be in discrete leaps.

## Slide 56: Perf. Trends: Bandwidth over latency
Bandwidth/throughput: total amount of work done in a given time
Latency/response time: the time between the start and the completion of an event.
Rule of thumb
  Bandwidth grow rate ~ improvement in latency2

## Slide 57: Performance milestones in microprocessor

## Slide 58: Challenges for IC Tecnology
IC characteristic: feature size
  10 microns in 1971  0.18microns in 2001
   0.09 microns in 2006  65nm
  40nm 28nm 14nm 7nm 5nm…
  Rule of thumb: transistor performance Improves linearly with decreasing feature size.
IC density improvement is both opportunity and Challenge:
  Signal delay for a wire increase in proportion to the product of its resistance and capacitance.
  Major design limitation: signal delay

## Slide 59: Topics in Chapter
1.1 Why take this course ?
1.2 Classes of computers in current computer market
1.3 Defining computer architecture and What’s the task of computer design?
1.4 Trends in Technology
1.5 Trends in power in Integrated circuits
1.6 Trends in Cost
1.7 Dependability
1.8 Measuring, Reporting and summarizing Perf.
1.9 Quantitative Principles of computer Design
1.10 Putting it altogether

## Slide 60: Trends in Power
Power also provide challenges as device scaled
  First microprocessor: 1/10 watt
  2GHz Pentium 4: 135 watt
Challenges:
  Distributing the power
  Removing the heat
  Preventing hot spot

## Slide 61
Pentium® 4 Processor
August 27, 2003
@3.2 GHz core
55 Million 0.13µ transistors
1249 SPECint2000
386 Processor
May 1986
@16 MHz core
275,000 1.5µ transistors
~1.2 SPECint2000
17 Years
200x
200x/11x
1000x

## Slide 62
Chart: Increase (X)
| Pipelined | S-Scalar | OOO-Spec | Deep Pipe
Area X | 4.2 | 3.5 | 2.1 | 2.3
Perf X | 2.4 | 2.9 | 1.7 | 1.8
Chart: Increase (X)
| Pipelined | S-Scalar | OOO-Spec | Deep Pipe
Power X | 1.3 | 2.4 | 2.1 | 2.2
Mips/W (%) | 0.78 | 0.19 | -0.16 | -0.17
Performance scales with area**.5
Power efficiency has dropped

## Slide 63: Two concepts
Dynamic power: power consumption in switching transistors.
  Power dynamic = ½ *Capacitive load * Voltage2 * Frequency switched
  Energy dynamic = Capacitive load * Voltage2
Static power: power consumption when a transistor is off due to power leakage
  Power static = current static * Voltage

## Slide 64: Rule of Thumb
10% reduction of voltage yields:
  10% reduction in frequency
  30% reduction in power
  Less than 10% reduction in performance
Voltage | Frequency | Power | Performance
1% | 1% | 3% | 0.66%
Rule of Thumb

## Slide 65: Dual core with voltage scaling
Frequency Reduction | Power Reduction | Performance Reduction
15% | 45% | 10%
Area = 1
Voltage = 1
Freq = 1
Power = 1
Perf = 1
Area = 2
Voltage = 0.85
Freq = 0.85
Power = 1
Perf = ~1.8
A 15%
Reduction
In Voltage
Yields
SINGLE CORE
DUAL CORE
RULE OF THUMB

## Slide 66: Multiple cores deliver more performance per watt
C1
C4
C2
C3
Small
core
Big core
Cache
Cache
1
2
3
4
1
2
1
1
1
2
3
4
1
2
3
4
Power
Performance
Many core is more power efficient
Power ~ area
Single thread performance ~ area**.5

## Slide 67
THANK YOU
THANK YOU