## Slide 1: Appendix C Basic pipeline concepts and implementation

## Slide 2: Pipelining RISC-V instruction set
Since there are five separate stages, we can have a pipeline in which one instruction is in each stage.
CPI is decreased to 1, since one instruction will be issued (or finished) each cycle.
During any cycle, one instruction is present in each stage.
Ideally, performance is increased five fold !

## Slide 3: Pipelined Datapath and Control
WB
MEM
Right-to-left flow leads to hazards

## Slide 4: Five stage pipeline
Need registers (or latch) between stages
  To hold information produced in previous cycle

## Slide 5: Pipeline Hazards
Taxonomy of Hazards
  Structural hazards
    These are conflicts over hardware resources.
  Data hazards
    Instruction depends on result of prior computation which is not ready (computed or stored) yet
  Control hazards
    branch condition and the branch PC are not available in time to fetch an instruction on the next clock

## Slide 6: How to solve the structural hazard
Multiple accesses to memory
  Split instruction and data memory / multiple memory port / instruction buffer
  Memory bandwidth need to be imporved by 5 folds.
Multiple accesses to the register file
  Double bump
Not fully pipelined functional units
  Fully pipeline the functional unit
  Using multiple functional unites
Real machine often with structural hazards.

## Slide 7: Summary of Structural hazard
Taxonomy of Hazards
  Structural hazards
    These are conflicts over hardware resources.
    OK, maybe add extra hardware resources;
    or full pipelined the functional units;
    otherwise still have to stall
    Allow machine with Structural hazard, since it happens not so often
  Data hazards
    Instruction depends on result of prior computation which is not ready (computed or stored) yet
  Control hazards
    branch condition and the branch PC are not available in time to fetch an instruction on the next clock

## Slide 8: Data hazard
Data hazards occur when the pipeline changes the order of read/write accesses to operands (Violation of data dependence) ycomparing with that in sequential executing, .
Let’s see an Example
  DADD R1, R1, R3
  DSUB R4, R1, R5
  AND R6, R1, R7
  OR R8, R1, R9
  XOR R10, R1, R11

## Slide 9: Coping with data hazards:example

## Slide 10: Data hazard
Basic structure
  An instruction in flight wants to use a data value that’s not “done” yet
  “Done” means “it’s been computed” and “it’s located where I would normally expect to go look in the pipe hardware to find it”
Basic cause
  You are used to assuming a purely sequential model of instruction execution
  Instruction N finishes before instruction N+k, for k >= 1
  There are dependencies now between “nearby” instructions (“near” in sequential order of fetch from memory)
Consequence+
  Data hazards -- instructions want data values that are not done yet, or not in the right place yet

## Slide 11: Somecases “Double Bump” can do !

## Slide 12: The simplest way to solve data hazard: stall
Proposed solution
  Don’t let them overlap like this…?
Mechanics
  Don’t let the instruction flow through the pipe
  In particular, don’t let it WRITE any bits anywhere in the pipe hardware that represents REAL CPU state (e.g., register file, memory)
  Let the instruction wait until the hazard resolved.
  Name for this operation: PIPELINE STALL

## Slide 13: How do we stall ? Insert nop by compiler
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble

## Slide 14: How do we stall? Add hardware Interlock !
Add extra hardware to detect stall situations
  Watches the instruction field bits
  Looks for “read versus write” conflicts in particular pipe stages
  Basically, a bunch of careful “case logic”
Add extra hardware to push bubbles thru pipe
  Actually, relatively easy
  Can just let the instruction you want to stall GO FORWARD through the pipe…
  …but, TURN OFF the bits that allow any results to get written into the machine state
  So, the instruction “executes” (it does the work), but doesn’t “save”

## Slide 15: Interlock: insert stalls
Bubble
Bubble
Empty slots in the
pipe called bubbles;
means no real
instruction work
getting saved here
How the interlock is implementated ?

## Slide 16: How the Interlock functions?
The Interlock can simulate the NOP:
  Once it is detected need to add a stall, then
  Clear the ID/EX.IR to be the instruction of NOP.
    disable the write signal: “wreg, wmem”.
  Keep IF/ID. IR unchanged for one more clock cycle.
    Disable the write signal: “WritePC, WriteIR”.

## Slide 17: How to Stall ? Add a stall control logic !
PC IF/ID ID/EX EX/MEM MEM/WB
F.Inst
D.Inst
E.Inst
M.Inst
Stall control logic
Rs
Rt
Wreg
Branch
Bubble
Wreg
Branch
Bubble
Rd
Rd
stall
To produce a stall signal. If stall ==1 then
Use stall to disable writing PC write and IF/ID latch.
Push a bubble into next stage.
  Bubble = 1 and disable control signal Wreg and Wmem.
  Puch a nop forward into ID/EX

## Slide 18: How to stall (when data hazard )?
If stall == 0 //stop the latter ones
  then PC  new PC; IF/ID.IR  IF.IR
  IF/ID.NPC  PC + 4
If stall == 1 // push bubble forward
  then ID/EX.nop 1 else ID/EX.nop 0
When initial
  ID/EX.nop 0, EX/MEM.nop  0, Mem.WB.nop 0
Are the stalls the same for
Data hazard / control hazard ?

## Slide 19: Solve the data hazard by Forwarding
Data Dependence
I2 RAW on I1
I3 RAW on I1
I4 RAW on I1
I5 RAW on I1
Data Hazard
I2 RAW hazard with I1
I3 RAW hazard with I1
RAW hazard，but no stall
using double bump
No RAW hazard

## Slide 20: Hardware Change for Forwarding
MEM/WR
ID/EX
EX/MEM
Data
Memory
ALU
mux
mux
Registers
NextPC
Immediate
mux
Source  sink
EX/Mem.ALUoutput  ALU input
MEM/WB.ALUoutput  ALU input
MEM/WB.LMD  ALU input
When to use the red. Blue
purple forwording path ?

## Slide 21: When to use the forwarding path ?
EX/Mem.ALUoutput  ALU input
    The previous instruction in EX/MEM is ALU
    The instruction in ID/EX has Rs1 or Rs2 source register
    EX/MEM.Rd == ID/EX.Rs1 or EX/MEM.Rd ==ID/EX.Rs2
MEM/WB.ALUoutput  ALU input
    The previous instruction in MEM/WB is ALU
    The instruction in ID/EX has Rs1 or Rs2 source register
    MEM/WB.Rd == ID/EX.Rs1 or MEM/WB.Rd == IF/ID.Rs2
MEM/WB.LMD  ALU input
    The previous instruction in MEM/WB is Load
    The instruction in ID/EX has Rs1 or Rs2 source register
    MEM/WB.Rd == ID/EX.Rs1 or MEM/WB.Rd == ID/EX.Rs2

## Slide 22: Forwarding at EX stage

## Slide 23: Fowarding can only solve some problems
ADD x6, x28, x29
SUB x30, x6, x14
ADD x6, x28, x29
AND x14, x5, x7
SUB x30, x6, x14
/ LW x6, 4(x10)

## Slide 24: Control hazard Example: Branches
R3, 24

## Slide 25: Recall: Basic Pipelined Datapath

## Slide 26: Control hazard

## Slide 27: Dealing with the control hazard
Four simple solutions
  Stall
  Prediction
    Predict-untaken: treat every branch as not taken
    Predict-taken: treat every branch as taken
    Delayed branch ( omit)
Note:
  Fixed hardware
  Compile time scheme using knowledge of hardware scheme and of branch behavior

## Slide 28: Recall: solve the hazard by inserting stalls
24
48 or 72

## Slide 29: Flushing the pipeline
Simplest hardware:
  Holding or deleting any instruction after branch until the branch destination is know.
  Penalty is fixed.
  Can not be reduced by software.
Implementation. Note difference with data hazard stall
  Stop the later instruction: keep PC unchanged
  Nop  IF/ID.IR clear the wrong instruction fetched
  Nop  ID/EX.IR push a bubble forward

## Slide 30: Stalls greatly hurt the performance
Problem:
  With a 30% branch frequency and an ideal CPI of 1, how much the performace is by inserting stalls ?
Answer:
  CPI = 1+30%３＝1.9
  this simple solution achieves only about half of the ideal performance.

## Slide 31: Always Stall Hurts the Not- taken case
24

## Slide 32: How about assume Branch Not Taken

## Slide 33: How to do with the branch taken ?
24

## Slide 34: Predict –not-taken
Hardware:
  Treat every branch as not taken (or as the formal instruction)
    When branch is not taken, the fetched instruction just continues to flow on. No stall at all.
    If the branch is taken, then restart the fetch at the branch target, which cause 3 stall.(should turn the fetched instruction into a no-op)
    Perf = 1+ br% ( not taken% * 0 + take%* 3 )
Compiler:
  Can improve the performance by coding the most frequent case in the untaken path.

## Slide 35: Implementation of predict-not-taken
When the branch is not taken, run as the branch is an ALU.
When the branch is taken， then
  Change the PC to the branch target ( turn to the right direction)
  Kill the wrong instructions have been predicted to execute.
    NopIF/ID
    NopID/EX
    NopEX/MEM

## Slide 36: Move the Branch Computation Forward

## Slide 37: Move the Branch Computation more Forward
store
load

## Slide 38: Example: Branch Taken

## Slide 39: Example: Branch Taken
What’s the possible problem ?

## Slide 40: Data Hazards for Branches
If a comparison register is a destination of preceding ALU instruction or 2nd preceding load instruction
  Need 1 stall cycle
beq stalled
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
ID
EX
MEM
WB
add x4, x5, x6
ld x1, addr
beq x1, x4, target

## Slide 41: Data Hazards for Branches
If a comparison register is a destination of immediately preceding load instruction
  Need 2 stall cycles
beq stalled
IF
ID
EX
MEM
WB
IF
ID
ID
ID
EX
MEM
WB
beq stalled
ld x1, addr
beq x1, x0, target

## Slide 42: Can the stalls on the previous page be reduced ?
Yes. Move the forwarding path from EX stage to ID stage.
though at the cost of Clock cycle time be increased.
Please note:
the positions of the sources /sinks of the forwarding paths.
Question: When the purple forwarding path will be needed ?

## Slide 43: Fowarding paths in Lab1